## Slide 1
מעבדה במחשבים מחומרה לתוכנה
קורס 10083
אריק גיספאן arikgi@post.jce.ac.il
הרצאה 2
Boolean Arithmetic

## Slide 2: Counting systems
quantity decimal binary 3-bit register
0 0 000
 1 1 001
 2 10 010
 3 11 011
 4 100 100
 5 101 101
 6 110 110
 7 111 111
 8 1000 overflow
 9 1001 overflow
 10 1010 overflow

## Slide 3: Rationale

## Slide 4
no overflow
overflow
Algorithm: exactly the same as in decimal addition
Overflow (MSB carry) has to be dealt with.
Binary addition
Assuming a 4-bit system:
1 1 1 1
1 0 1 1
0 1 1 1
1 0 0 1 0
0 0 0 1
1 0 0 1
0 1 0 1
0 1 1 1 0

## Slide 5: Representing negative numbers (4-bit system)
The codes of all positive numbers begin with a “0”
The codes of all negative numbers begin with a “1“
To convert a number: leave all trailing 0’s and first 1 intact, and flip all the remaining bits
0 0000
1 0001 1111 -1
2 0010 1110 -2
3 0011 1101 -3
4 0100 1100 -4
5 0101 1011 -5
6 0110 1010 -6
7 0111 1001 -7
1000 -8
Example: 2 - 5 = 2 + (-5) = 0 0 1 0
+ 1 0 1 1
1 1 0 1 = -3

## Slide 6: Building an Adder chip
Adder: a chip designed to add two integers
Proposed implementation:
  Half adder: designed to add 2 bits
  Full adder: designed to add 3 bits
  Adder: designed to add two n-bit numbers.

## Slide 7: Half adder (designed to add 2 bits)
Implementation: based on two gates that you’ve seen before.
a b carry sum
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0

## Slide 8: Full adder (designed to add 3 bits)
Implementation: can be based on half-adder gates.
a b c carry sum
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1

## Slide 9: n-bit Adder
Implementation: array of full-adder gates.
... 1 0 1 1 a
… 0 0 1 0 b
… 1 1 0 1 out
+

## Slide 10: The ALU (of the Hack platform)
out(x, y, control bits) =
x+y, x-y, y–x,
0, 1, -1,
x, y, -x, -y,
x!, y!,
x+1, y+1, x-1, y-1,
x&y, x|y

## Slide 11: ALU logic (Hack platform)
Implementation: build a logic gate architecture that “reads” each control bit and does what the table specifies: if zx=1 then set x to 0, etc.

## Slide 12
The ALU in the CPU context (Hack platform)
ALU
Mux
D
out
A/M
a
D register
A register
A
M
c1,c2, … ,c6
RAM
(selected register)

## Slide 13: Perspective
Combinational logic
Our adder design is very basic: no parallelism
It pays to optimize adders
Our ALU is also very basic: no multiplication / division
Where is the seat of advanced math operations? a typical hardware/software tradeoff.

## Slide 14: Historical note: Leibnitz (1646-1716)
“The binary system may be used in place of the decimal system; express all numbers by unity and by nothing”
1679: built a mechanical calculator (+, -, *, /)
CHALLENGE: “All who are occupied with the reading or writing of scientific literature have assuredly very often felt the want of a common scientific language, and regretted the great loss of time and trouble caused by the multiplicity of languages employed in scientific literature:
SOLUTION: “Characteristica Universalis”: a universal, formal, language of reasoning
The dream’s end: Turing and Goedl in 1930’s.
Leibniz’s medallion for the Duke of Brunswick