## Slide 1: Computer Architecture
Based on “The Elements of Computing Systems”, Nisan & Schocken, MIT Press, forthcoming in 2004, www.idc.ac.il/tecs
project 11
Yana Gabelev

## Slide 2: Links
Project 11:
http://my.jce.ac.il/~arikgi/Web/Ex/Ex11/index.htm
EX10 zip :
http://my.jce.ac.il/~arikgi/Web/Ex/Ex11/Ex11.zip

## Slide 3: von-Neumann Architecture
The model describes the architecture of almost all digital computers.

## Slide 4: Implementation
Implement all the following gates:
Memory | DFF3Step
CPU | 
Computer | 

## Slide 5: Memory
The Memory chip of the Hack platform is essentially a package of three lower-level chips: RAM16K, Screen, and Keyboard.

## Slide 6: RAM 16K
Chip name: RAM16K // Memory of 16K registers
Inputs: in[16], address[14], load
Outputs: out[16]
Function: out(t)=RAM[address(t)](t)
If load(t-1) then RAM[address(t-1)](t)=in(t-1)
Comment: “=” is a 16-bit operation.
14

## Slide 7: Keyboard interface
Chip name: Keyboard // Memory map of the physical keyboard.
// Outputs the code of the currently
// pressed key.
Outputs: out[16] // The ASCII code of the pressed key, or
// one of the special codes, or 0 if no key is
// pressed.
Function: Outputs the code of the key presently pressed on the
physical keyboard.

## Slide 8: Screen interface
Chip name: Screen // Memory-map of the physical screen
Inputs: in[16], // What to write
load, // Write-enable bit
address[13] // Where to write
Outputs: out[16] // Screen value at the given address
Function: Functions exactly like a 16-bit 8K RAM:
1. out(t)=Screen[address(t)](t)
2. If load(t-1) then Screen[address(t-1)](t)=in(t-1)
(t is the current time-unit, or cycle)

## Slide 9: Memory
Chip name: Memory // Complete memory address space
Inputs: in[16], // What to write
load, // Write-enable bit
address[15] // Where to write
Outputs: out[16] // Memory value at the given address
Function: 1. out(t)=Memory[address(t)](t)
2. If load(t-1) then Memory[address(t-1)](t)=in(t-1)
(t is the current time-unit, or cycle)
Comment: Access to address>0x6000 is invalid. Access to any address in the range 0x4000–0x5FFF results in
accessing the screen memory map. Access to address
0x6000 results in accessing the keyboard memory
map. The behavior in these addresses is described in
the Screen and Keyboard specifications.

## Slide 10: CPU (Central Process Unit)
Notes: הליבה של המחשב. אחראי על ביצוע הפעולות של התוכנה המופעלת. ההוראות הללו גורמות למחשב לבצע חישובים לקרוא ולכתוב לזיכרון- בעזרת ALU רגיסטרים ויחידת שליטה
Data registers: These registers give the CPU short-term memory services. For example, when calculating the value of (a-b)*c, we must first compute and remember the value of (a-b). Although this result can be temporarily stored in some memory location, a better solution is to store it locally inside the CPU – in a data register.
Addressing registers: The CPU has to continuously access the memory in order to read data and write data. In every one of these operations, we must specify which individual memory word has to be accessed, i.e. supply an address. In some cases this address appears as part of the current instruction, while in others it depends on the execution of a previous instruction. In the latter case, the address should be stored in a register whose contents can be later treated as a memory address -- an addressing register.
Program Counter (PC) register: When executing a program, the CPU must always keep track of the address of the next instruction that must be fetched from the instruction memory. This address is kept in a special register called program counter, or PC. The contents of the PC are then used as the address for fetching instructions from the instruction memory. Thus, in the process of executing the current instruction, the CPU updates the PC in one of two ways. If the current instruction contains no “goto” directive, the PC is incremented to point to the next instruction in the program. If the current instruction includes a “goto n” directive, the CPU loads n into the PC.

## Slide 11: CPU Components and Function
CPU components: ALU + A, D, PC registers
CPU Function:
The M value is read from inM
The D and A values are read from (or written to) these CPU-resident registers
If the instruction wants to write to M (e.g. M=D), then the M value is placed in outM, the value of the CPU-resident A register is placed in addressM, and writeM is asserted
If reset=1, then pc is set to 0; Otherwise, pc is set to the address resulting from executing the current instruction.

## Slide 12: CPU
dest = comp ; jump
comp dest jump
binary: 1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
zx nx zy ny f no A D M <0 =0 >0
When:
a=0 → A
a=1 → M
Notes: Jmp – מקודד ל-PC
Dest – מקודד למוצא ה-ALU
Comp – מקודד בתוך ה-ALU
a- מקודד ב-MUX שנמצא לפני ה-ALU (אחת הכניסות ל-ALU)
The diagram shows only data and address paths, i.e. wires that carry data and addresses from one place to another. The diagram does not show the CPU’s control logic, except for inputs and outputs of control bits, labeled ©. Thus it should be viewed as an incomplete chip diagram.

## Slide 13: Instruction decoding
Get type of instruction "i xx a cccccc ddd jjj“.
  The i-bit codes the instruction type, which is '0' for an A-instruction and '1' for a C-instruction.
The a-bit and the c-bits represent the comp part, the d-bits represent the dest part, and the j-bits represent the jump part of the instruction.
In case of an A-instruction, the 15 bits other than the i-bit should be interpreted as a 15-bit constant.

## Slide 14: Instruction execution
The various fields of the instruction (i-, a-, c-, d-, and j-bits) are routed simultaneously to various parts of the architecture, where they cause different chips to do what they are supposed to do in order to execute either the A-instruction or the C-instruction, as mandated by the machine language specification.
In particular, the a-bit determines whether the ALU will operate on the A register input or on the Memory input, the c-bits determine which function the ALU will compute, and the d-bits enable various locations to accept the ALU result.

## Slide 15: Next instruction fetching
The CPU also determines the address of the next instruction and emits it via its pc output. The programmer wants the computer to fetch and execute the next instruction in the program. Thus if t is the current time-unit, the default program counter operation should be PC(t)=PC(t-1)+1.
When we want to effect a goto n operation, the machine language specification requires to first set the A register to n (via an A-instruction) and then issue a jump directive (coded by the j-bits of a subsequent C-instruction).

## Slide 16
This is a function of two signals: (a) the j-bits of the current instruction, specifying on which condition we are supposed to jump, and (b) the ALU output status bits, indicating whether the condition is satisfied. If we have a jump, the PC is loaded with A's output. Otherwise, the PC increments by 1.
Additionally, if we want the computer to re-start the program's execution, all we have to do is reset the program counter to 0.
Next instruction fetching

## Slide 17: Computer
Once the CPU and the Memory chips have been implemented and tested, the construction of the overall computer is straightforward.
Notes: Computer = ביט 1 של קלט
הצ'יפ העליון בהיררכיה. מכיל CPU RAM ROM מסך מקלדת בתור חלקים פנימיים.
צריך לטעון צ'יפ ROM למחשב כדי להריץ תוכנית. אפשר לשלוט על מסך ומקלדת דרך מיפוי הזיכרון שלהם.

## Slide 18
Computer
Notes: לצ'יפ הCOMPUTER אין פלט (output)

## Slide 19
Chip name: Computer // Top-most chip in the Hack platform
Inputs: reset
Function: When reset is 0, the program stored in the computer's
ROM executes. When reset is 1, the execution of the
program restarts. Thus, to start a program’s execution,
reset must be pushed “up” (1) and “down” (0).
From this point onward the user is at the mercy of the
software. In particular, depending on the program's
code, the screen may show some output and the user
may be able to interact with the computer via the
keyboard.
Computer
Notes: לצ'יפ הCOMPUTER אין פלט (output)

## Slide 20
Chip name: DFF3Step
Inputs: in[16]
Output: a[16],b[16],c[16]
Function: This chip is an extended DFF: remembers not only last
input, but three a(t) = in(t-1)
b(t) = in(t-2)
c(t) = in(t-3)
Twist

## Slide 21: How and what to submit
Create a folder named 2015B_exXX_YYYYYYYY, when XX is the ex number, and YYYYYYYY is your ID.
For example: 2015B_ex11_123456789
All submission files should be in that folder, and no other extra file. Files to submit: HDL files, README.txt
Zip the folder to a zip file named 2015B_exXX_YYYYYYYY.zip